## Slide 1
PROGRESS PRESENTATION / V0.1
From Rhino model to grounded design.
How ParkHaven Studio works
Local analysis • controlled evidence • bounded AI • printable report
4 MIN
Notes: ParkHaven Studio turns a Rhino massing model into a traceable design review. The goal is not to replace the designer. It is to connect geometry, repeatable Grasshopper calculations, clear visual evidence, and bounded AI advice in one local workflow. The current prototype already handles a real Parkhaven model, produces controlled views and metrics, and exports an English PDF report. Everything shown today runs around Rhino 8 on the designer's Windows workstation.

## Slide 2
END-TO-END WORKFLOW
One model, five controlled gates
02
01
Import
Preserve and hash the source 3DM
02
Position
Approve coordinates and model units
03
Analyze
Run Rhino + Grasshopper locally
04
Evidence
Capture views and bounded metrics
05
Report
Review advice and export PDF
Every output is linked to the approved run. Stale or incomplete evidence stops here.
PARKHAVEN STUDIO
LOCAL • TRACEABLE • MODEL-GROUNDED
Notes: The workflow has five controlled steps. First, the designer imports a 3DM file. The app hashes and preserves that source, then works only on a copy. Second, the designer positions the model and approves its units. Third, Rhino and Grasshopper run the analysis. Fourth, the app captures four standardized model views and combines those with calculated metrics for optional AI review. Finally, the app builds a printable report. Each transition has a gate, so incomplete placement, stale evidence, or failed analysis cannot silently flow into the final output.

## Slide 3
LOCAL ARCHITECTURE
Deterministic calculation, bounded interpretation
03
SOURCE
Rhino .3dm
unchanged + SHA-256
DESKTOP APP
Local backend
isolated run folder
CALCULATION
Rhino + Grasshopper
visible, repeatable solve
EVIDENCE
JSON + four views
hash-linked artifacts
OUTPUT
PDF review
metrics + hypotheses
AUTHORITATIVE
Grasshopper metrics
OPTIONAL AI
Bounded text only — images stay local
PARKHAVEN STUDIO
LOCAL • TRACEABLE • MODEL-GROUNDED
Notes: The architecture is intentionally local-first. The desktop shell starts an authenticated local backend. That backend creates an isolated run folder and launches Rhino visibly, using a packaged Grasshopper definition. Grasshopper writes the scene, geometry summary, and result JSON; the app verifies their hashes before displaying them. Only a bounded text evidence package can go to an OpenAI-compatible endpoint. The model images remain local. This separation makes it clear which values came from deterministic calculation and which statements are AI hypotheses.

## Slide 4
MODEL EVIDENCE
Stable colors replace floating labels
04
TOP VIEW
OVERVIEW
Volume A
Volume B
Volume C
4 cameras • 768 × 512 • analysis overlays hidden
PARKHAVEN STUDIO
LOCAL • TRACEABLE • MODEL-GROUNDED
Notes: This is the evidence layer from the real massa fase 2 model. The exporter gives each analytical mass a stable color: Volume A is blue, B orange, and C purple. The viewer then captures top, overview, facade-side, and park-side cameras at a fixed resolution. Analysis overlays are hidden in those evidence images so the masses remain readable, while the measured results stay available in the dashboard. The report uses the same color legend instead of floating point labels, which makes every referenced volume easy to identify across all views.

## Slide 5
SCREENING RESULTS
Numbers for comparison, not final engineering
05
GROSS FLOOR AREA
51,868 m²
VISIBILITY
24.5%
INDICATIVE COST
€ 93.4 million
CLIMATE SCREENING
Mean sun hours
4.3 h
Maximum UTCI
18.5 °C
Sunlit area
78.9%
FOUNDATION SCREENING
249
load-based piles
6.0 m
grid centres
INDICATIVE — requires engineering verification
PARKHAVEN STUDIO
LOCAL • TRACEABLE • MODEL-GROUNDED
Notes: The analysis produces decision-ready screening metrics. In this run the gross floor area is about fifty-one thousand nine hundred square metres, visibility is twenty-four point five percent, and indicative cost is ninety-three point four million euros. The climate screen reports four point three mean sun hours and a maximum UTCI of eighteen point five degrees for one selected weather condition. Foundation screening estimates two hundred forty-nine load-based piles. These are transparent screening values, not final engineering design, and the report labels that limitation explicitly.

## Slide 6
TRUST CONTROLS
The app blocks unsupported conclusions
06
SOURCE
Original 3DM unchanged
SHA-256 linked
EVIDENCE
Current run only
scene + metrics + views
POLICY
Site constraints unavailable
no horizontal movement
AI PROPOSAL
“Shift Volume A toward the tunnel”
BLOCKED
no verified envelope
Allowed: test changes within the current footprint
PARKHAVEN STUDIO
LOCAL • TRACEABLE • MODEL-GROUNDED
Notes: Trust controls are part of the product, not an afterthought. The original 3DM stays unchanged, and every run carries source, definition, weather, scene, and evidence hashes. A report only accepts advice tied to the current evidence and current policy version. We also found no authoritative plot, access, or tunnel envelope in the available data. Therefore the server rejects advice to shift, widen, set back, or rotate a mass. The AI can propose tests within the current footprint, but it cannot invent site clearance from an aerial photograph.

## Slide 7
CURRENT PROGRESS / OCTOBER 2026
Working end to end.
Verified with the real Parkhaven massing model
127
APP TESTS
25
ANALYZER TESTS
4
CONTROLLED VIEWS
2
PDF PAGES
PASS
INSTALLED BUNDLE
NEXT
Authoritative site constraints
Signed distribution
Clean-machine acceptance
VISUAL • MEASURABLE • AUDITABLE
Notes: The current build has passed one hundred twenty-seven app tests, twenty-five analyzer tests, real Rhino acceptance, four controlled WebGL captures, installed-bundle smoke testing, and a two-page PDF review. The installer and report workflow are working end to end. The next major step is to add authoritative site constraints, followed by signed distribution and clean-machine acceptance. In short, ParkHaven Studio now provides a usable bridge from Rhino geometry to a review that is visual, measurable, and auditable.